## Slide 1: Freeform based optical designs
Gabby Kroes, Tibor Agócs, Felix Bettonvil
NOVA Optical Infrared Instrumentation Group at ASTRON, P.O. Box 2, 7990 AA, The Netherlands.

## Slide 2: NOVA
Optical Infrared Group

## Slide 3: NOVA - Optical InfraRed Group

## Slide 4: Work methodology
Concurrent
Engineering
Optical
Mechanical
Thermal
Electrical
Software
NOVA Optical Infrared instrumentation group (Netherlands)
Concurrent engineering
Plan design-manufacturing-alignment-verification cycle
Find the optimum (best trade-off)
Design
Manufacture
Alignment
Verification

## Slide 5: Introduction
Freeform design, manufacturing, testing

## Slide 6: Introduction
Freeform surface based systems offer
  More degrees of freedom
  Superior image quality
  Compact designs
    smaller space envelope, lower weight
  Less number of surfaces
  Generally better solutions when the symmetry of the system is broken
  Tailor made optimizations (dedicated merit function targeting system geometry, distortion, etc)
New way of thinking is needed in
  Optical design
  Manufacturing
  Testing

## Slide 7: Introduction
Freeform optical design
  Existing methods mostly for non-imaging applications (car head lamps, illumination, solar collector)
  NOVA developed freeform optical design methods for imaging applications (collimators, cameras, relays, etc.)
Freeform manufacturing
  Diamond turning, nickel plating
  Stress polishing
  Hydroforming
Freeform testing
  Tactile measurements
  Shack Hartmann
  Deflectometry

## Slide 8: Freeform based optical design examples (NOVA)
METIS SMO, two-, three-mirror systems, reflective Alvarez

## Slide 9: Freeform based optical designs
METIS LM band spectrograph
Double pass three mirror anastigmat
Re-optimized design with freeform M3, all other surfaces are spherical
M1 spherical
M2 spherical
M3 freeform
IG
55 mm
50 mm
PV 10.2µm, RMS 1.2µm deviation from BFS

## Slide 10: Freeform based optical designs
M2 (freeform)
Entrance pupil
F1.5 Two mirror system

## Slide 11: Freeform based optical designs
M1 freeform
M2 spherical
M3 spherical
F2 Three mirror system

## Slide 12: Freeform based optical designs
M1 freeform
M4 freeform
Complete spectrograph (220mm pupil, 176mm slit, F1.8 camera)

## Slide 13: Freeform based optical designs
Reflective Alvarez
Side view
Classical Alvarez

## Slide 14: Freeform based optical designs
Reflective Alvarez
Top view
Classical Alvarez

## Slide 15: Freeform based optical designs
Reflective Alvarez
M1
M2
M1-M2

## Slide 16: Freeform work methodolgy
Concurrent engineering

## Slide 17: AM and optical systems design
To achieve the best results with respect to the freeform based optical system
  System optimization is needed
  Concurrent engineering
From the perspective of the optical design knowledge is inevitable on
  Manufacturing processes, limitations, capabilities
  Testing strategy, testing equipment, etc.

## Slide 18: interests
Use available knowledge
  @ NOVA
  FAME
Integrated instrument design
  Advance on our concurrent design philosophy
Better instrumentation
  High(er) quality
  Smaller
  Lighter
  Manufacturing, Assembly, Integration, Test, Handling and Transport